## Slide 1: Structured sparse acoustic modeling for speech separation
Afsaneh Asaei
Joint work with: Mohammad Golbabaee,
Herve Bourlard, Volkan Cevher

## Slide 2
φ21
φ52
s1
s2
s3
s4
s5
x1
x2
φ11
φ42
Speech Separation Problem
SPARSITY is essential to deal with the
ill-posed source separation problem

## Slide 3: Listening results
http://www.idiap.ch/~aasaei/MONC-Demo.html

## Slide 4: Key idea
  Incorporation of acoustic channel model for speech separation
    Cast speech separation problem as spatio-spectral information recovery from compressive acoustic measurements
Structured Sparse Speech Representation
Acoustic Reverberation Models
Microphone Array
Speech Separation
Structured Sparse Acoustic Modeling

## Slide 5: Spectrographic Speech
Source 1
Source 2
Source 3
Overlapping speech
N sources
M sensor
< M source
< M source
Spectral Sparsity

## Slide 6: Spectral sparsity
Compressibility of speech information bearing
components
  Enables high accuracy
  speech recognition
original spectrogram
auditory spectrogram
Figs. Ref. “Hearing is Believing”, R. Stern and N. Morgan, IEEE SPS Mag. Nov. 2012

## Slide 7: Spectral sparsity
Disjointness of overlapping spectrographic speech
Histogram of the energy of point-wise multiplication
of two histograms of independent sources
Diagonal Gram matrix

## Slide 8
X21 | X22 | X23 | X24 | X25
X16 | X17 | X18 | X19 | X20
X11 | X12 | X13 | X14 | X15
X6 | X7 | X8 | X9 | X10
X1 | X2 | X3 | X4 | X5
Spatial sparsity
Discretization of the planar area of the room
      Location of sound sources is sparse
X21 | X22 | X23 | X24 | X25
X16 | X17 | X18 | X19 | X20
X11 | X12 | X13 | X14 | X15
X6 | X7 | X8 | X9 | X10
X1 | X2 | X3 | X4 | X5

## Slide 9
objective
    Spatio-spectral sparse representation of overlapping speech sources
    GOAL: Model the acoustic reverberant channel
Number of Microphones
Number of cells on a Grid

## Slide 10: multipath channel
Reflection coefficient
Speed of sound
Sensor location
Source location
Number of reflections
  Microphone array measurement matrix
    Image Model and Green’s function of sound propagation

## Slide 11: Reverberant acoustic
Structured sparsity underlying multipath propagation
Spatial sparsity
  actual sources
Structured sparsity
  actual-virtual sources
Image Map

## Slide 12: factorized formulation
New factorized formulation of multipath acquisition
Free-space Green’s function matrix
Permutation map; Actual sources  actual/virtual sources
Source matrix; spatio-spectral content of frames
at a given frequency
Image map of ith source
X
O
S
=
P

## Slide 13: Measurement correlation
Structured sparsity underlying correlation matrix
Goal: estimation of
  Enables source localization and absorption coefficients estimation

## Slide 14: group sparse representation
Kronecker product property
Kronecker product
Element-wise conjugate
(number of sources) groups of contain nonzero elements
  Identifying those groups determines source location
  Recovering the corresponding elements of and normalization by source energy determines absorption coefficients

## Slide 15: joint localization & absorption coefficient estimation
Group sparse recovery

## Slide 16: Room impulse response

## Slide 17: Numerical evaluations
Multichannel overlapping numbers corpus (MONC)
  Numbers corpus are played back
  Recorded by 8-channel circular array in a room 8.2m×3.6m×2.4m
  Reverberation time is 300 ms
  Inverse filtering the acoustic channel following by linear post-filtering to enhance the separated signals

## Slide 18: Absorption coefficients

## Slide 19: Word recognition rate
Chart: Word Recognition Rate%
| Two speakers | Three speakers
Baseline | 55.19 | 39.92
Lapel | 74.53 | 68.13
Superdirective BF | 68.16 | 61.45
Room Acoustic Modeling | 87.93 | 79.21

## Slide 20: Perceptual quality
Chart: PESQ
| Two speakers | Three speakers
Baseline | 2 | 1.6
Lapel | 2.35 | 2.27
Superdirective BF | 2.69 | 2.48
Room Acoustic Modeling | 2.8 | 2.62

## Slide 21: Concluding remark
  Characterization of the acoustic measurements for reverberant enclosures enables acoustic-aware source separation
    High quality and recognition rate
  Estimation of the reflections and attenuations for an unconstrained environment
    Reconstruction of the sound field using plenacoustic function
  Calibration of the acoustic measurement model
  Non-uniform sampling the acoustic field
    Extension to continuous sources
  Incorporation of signal dependent models and low-rank structures
  Post-processing of the signal recovery residual error

## Slide 22
  J. B. Allen and D. A. Berkley, “Image method for efficiently simulating small-room acoustics,” Journal of Acoustical Society of America, vol. 60(s1), 1979.
  A. Asaei, M. Golbabaee, H. Bourlard, and V. Cevher, “Structured Sparsity Models for Multiparty Speech Recovery from Convolutive Recordings,” TASL submission, 2012.
  “Can one hear the shape of a room: The 2-D polygonal case”, I. Dokmanic, Y. M. Lu and M. Vetterli, ICASSP 2011.
  A. Asaei, H. Bourlard, and V. Cevher, “Model-based compressive sensing for multi-party distant speech recognition,” in Intl. Conference on Acoustic Speech and Signal Processing (ICASSP), 2011.
  “The Multichannel Overlapping Numbers Corpus,” Idiap resources available online:, http://www.cslu.ogi.edu/corpora/monc.pdf
references
Thank you!